## Slide 1: IoT Device Workshop
All Resources and PowerPoint:
https://github.com/hess105/IoT-Workshop
Please Clone the Repository

## Slide 2: Internet of Things (IoT) Explained
Definition
  The network of interconnected devices that collect and exchange data over the internet
Key Components
  Devices
  Connectivity
  Data Processing
  Could Infrastructure

## Slide 3: Applications of IoT
Smart Homes
  Thermostats, lighting systems, anything controlled remotely
Industrial Monitoring
  Ability to monitor and track equipment and machinery
Healthcare Applications
  Wearable devices collecting healthcare data constantly
Smart Cities
  Better traffic systems, waste management
Agriculture

## Slide 4: Hardware

## Slide 5: Raspberry Pi Pico
Developed by the Raspberry Pi Foundation
Cost effective
RP2040 Microcontroller Chip
  Dual-Core ARM Cortext-M0+ @133 MHz
  26 GPIO
  2 MB onboard flash memory

## Slide 6: Pico Vs. Arduino
Arduino Nano
Clock Speed: 16 MHz
Flash Memory: 32 KB
GPIO Pins: 22
Cost: $10- $15
RP2040 Pico
Clock Speed: 133 MHz
Flash Memory: 2 MB
GPIO Pins: 26
Cost: $4 - $5
Notes: Discuss why we chose to use the Pico for this lab. Make sure to express board choice is usually a preference and dictated by the restrictions and needs of the project.

## Slide 7: Understanding GPIO
UART (TX / RX)
I2C (SDA / SCL)
SPI (SCK, TX, RX ,Csn)
GP0-GP15

## Slide 8: UART (Universal Asynchronous Receiver/Transmitter)
UART
  A serial communication protocol used for point to point communication.
  Uses two lines: TX (Transmit) and RX (Receive)
  Asynchronous (no clock signal shared)
  Very simple but effective means of communication

## Slide 9: I2C (Inter-Integrated Circuit)
I2C
  A serial communication protocol for connecting multiple peripherals.
  Uses two lines: SDA (Serial Data Line) and SCL (Serial Clock Line)
  Supports multiple devices on the same bus.
  Communication initiated by master device.

## Slide 10: SPI (Serial Peripheral Interface)
SPI
  A serial communication protocol for higher speed communication.
  Uses four lines:
    SCK (Serial Clock)
    MOSI (Master Out Slave In)
    MISO (Master In Slave Out)
    CSn (Chip Select)
  Supports multiple devices on the same bus.
  Synchronous as it has a clock

## Slide 11: Pico Pinout

## Slide 12: Software

## Slide 13: Arduino Software
C/C++ based software program for microcontrollers.
Pros:
  Beginner Friendly
  Widely supported
Cons:
  Optimization issues
  Restrictive program format

## Slide 14: The MicroPython Platform
What is it?
  A software implementation of Python 3 Programming language for microcontrollers.
Why Use it?
  Lightweight
  Python Compatibility
  Lots of Libraries and Support
  Cross Platform Support
Resources
  Official MicroPython website: micropython.org

## Slide 15: Our IDE of Choice: Thonny
What is Thonny?
  An IDE (Integrated Development Environment) designed for Python and Micropython Development
Why Thonny?
  Beginner Friendly
  Lightweight and Fast
  Lots of Support

## Slide 16: Install Thonny
https://thonny.org/

## Slide 17: Pico Firmware
Microcontroller Firmware
  Multiple supported languages:
    MicroPython
    CircuitPython
    C/C++
    Rust?
  This means we need to flash the firmware for our preferred language

## Slide 18: Flashing the Pico
https://github.com/hess105/IoT-Workshop/tree/main/MicroPython-Framework

## Slide 19: Micropython Basics
https://github.com/hess105/IoT-Workshop/tree/main/MicroPython-Framework/The-Basics

## Slide 20: LED Program

## Slide 21: Basics of Sensors

## Slide 22: DHT11
Low cost digital temperature and humidity module
  0 – 50 C (+/- 2 C)
  20 – 90% Humidity (+/- 5%)
Contains a thermistor for temperature and capacitive humidity sensor.
3 Pins
  VCC
  DATA
  GND
So what communication protocol does it use?
What Pins would we connect it to?

## Slide 23: 128 x 64 OLED Screen
Monochrome and Low Power Display
4 Pins
  VCC
  GND
  SCL
  SDA
So what communication protocol does it use?
What Pins would we connect it to?

## Slide 24: Importing Libraries
For additional functionality we will use libraries.
  Built-In Libraries can be included with only the import command
  Third-Party Libraries need to be physically added to the IDE in Thonny.
Keep in mind the limited memory available on microcontrollers when importing libraries. Avoid unnecessary imports to conserve memory.

## Slide 25: Reading Sensor Data
https://github.com/hess105/IoT-Workshop/tree/main/Project-2

## Slide 26: Wireless Communication
Transmission of data between devices without physical wires
Key Technologies
  Wifi (IEEE 802.11)
  Bluetooth (Short Range)
  LoRA (Long Range)
  Cellular (3G, 4G, 5G)

## Slide 27: LoRa and LoRaWAN
LoRa
  Proprietary wireless modulation technology developed by Semtech.
  Long-range communication with low-power consumption (several Kilometers line of sight)
LoRaWAN
  Protocol built upon LoRa physical layer that defines the communication protocol and network architecture.
  Enables secure bi-directional communication with router like devices.

## Slide 28: ThingSpeak
Open-Source IoT Platform
  Developed by MathWorks (same people as MATLAB)
Key Features
  API and libraries for collecting data from IoT devices
  Provides a spot for data storage
  Data visualization and analysis tools
Uses
  Environmental Monitoring, Home Automation, Smart Agriculture

## Slide 29: ESP32
Dual-Core Processor: ESP32 features two Tensilica LX6 CPU cores, offering high performance and efficiency.
  Variable Clock Speed (80 – 240 MHz)
Wi-Fi: Built-in Wi-Fi support, including 802.11b/g/n Wi-Fi standards
Bluetooth: Integrated Bluetooth 4.2 and Bluetooth Low Energy (BLE)
Low Power Consumption

## Slide 30: ThingSpeak Integration w/ ESP32
https://github.com/hess105/IoT-Workshop/tree/main/Project-3